## Slide 1
Start
Scoop servo and arm motor work to locate edge of scoop at edge of dump zone using calculated coordinates
Arm extends to push scoop towards opposite edge of dump zone
LED is deactivated. All motion should have ceased by now
End
Arm lowers and scoop levels out to carefully hold the rocks
Arm base swivels 135 degrees or so left and the system drives forward approx. 1300 mm
Arm raises to approx. 45 degrees from horizontal. Scoop servo is dynamically lowered to account for new arm angle (keeping the scoop at an acceptable angle to secure the rocks)
Arm extends to full required length found from necessary calculations to locate the scoop directly over the hopper. Scoop wall mechanism should mechanically activate.
Scoop servo is slowly rotated until the scoop funnel is 60 degrees below horizontal and in line with the hopper. The rocks should now fall uniformly into the hopper
Wheel motors are now activated in reverse to return the system to the end zone
Arm is retracted as necessary to fit within end zone
LED is activated to indicate run is currently going